## Slide 1: Optimizing For Hardware Transform and Lighting
Sim Dietrich
NVIDIA Corporation
sdietrich@nvidia.com

## Slide 2: HW T&L : The Good News
Hardware T&L is extremely fast
  GeForce2 GTS can achieve 22 million drawn triangles per second – Quadro2, Ultra even more
Using Hardware T&L correctly is very easy
  In DX7, it all happens through VertexBuffers

## Slide 3: HW T&L : The Bad News
Using HW T&L incorrectly is even *easier* than getting it right
  Some apps are slower when first ported to T&L!
Why? Because the obvious way to use VBs is NOT the right way
  If you replace many DrawPrimitive calls with many DrawPrimitiveVB calls, you will be very disappointed

## Slide 4: HW T&L : A New API Path
The “D3D TnL HAL” Device is new for DX7
It allows access to :
  AGP and video memory vertex buffers
  HW Texture Matrix
  HW Texture Coordinate Generation “TexGen”
  HW Fog
  HW Lighting
  HW Clipping
  HW Transform & Projection

## Slide 5: The D3D TnL HAL
The TnL HAL is a different API and driver path than the HAL
It has different Performance Characteristics
  Even more oriented towards batching than the HAL
  Higher memory overhead for VBs
    They are DDraw Surfaces, so have a 2K memory overhead
  Very expensive to create VBs
  Has the potential to be lighter-weight and faster than the HAL

## Slide 6: What is a Vertex Buffer, Anyway?
There are two answers to this question, one for Static VBs, and one for Dynamic VBs
Static VBs are like textures. You create them at level load time in AGP or video memory and leave them there
  Great for terrain, rigid-body objects
  Not good for skinned, animated characters or procedural effects
  NEVER create a VB at runtime – it can take 100s of milliseconds

## Slide 7: Vertex Buffers are Write Only
They are not designed for getting results back with ProcessVertices()
You can never get the result of T&L back
But that’s OK
  If you need to do collision detection or culling, you’d do best to use a separate simpler database anyway
    Case in point – Do you really need to walk through U,Vs & diffuse colors when doing collision work?
VBs should always be WRITE_ONLY – even on non T&L devices

## Slide 8: Dynamic VBs
Dynamic VBs are sort of like like streaming DVD video
  There is not enough space to hold every possible frame of animation, just like there wouldn’t be enough space to hold a DVD video in ram
  Plus, many effects are truly dynamic and have an essentially infinite number of possible states
  The focus is on getting the vertex data from the app to the card as efficiently as possible

## Slide 9: The Myths Of Dynamic VBs
If your data isn’t static, you can’t use T&L
  Wrong, VBs were designed to handle Dynamic data, too
Dynamic T&L is so slow as to be worthless
  Totally incorrect, Dynamic T&L is still faster than static CPU T&L
It is hard to manage Dynamic VBs
  I have a single page of source code to prove this one wrong…

## Slide 10: Shared Resources
The GPU is a co-processor to the CPU
If you can keep both processors busy, speed will be excellent
However, to work together, the CPU and GPU must sometimes share resources
  Textures
  Frame Buffers
  Vertex Buffers
If the sharing is managed poorly, you will get no overlap between the GPU and CPU and performance will suffer

## Slide 11: Keeping GPU & CPU Busy
Dynamic VBs are a shared resource
CPU must write data into it
GPU must read data out of it
The API tries to ensure that both of these won’t occur in the same place at the same time
You can control how strictly access to the VB is managed
Control is managed through three flags :
  DDLOCK_WRITEONLY
  DDLOCK_DISCARDCONTENTS
  DDLOCK_NOOVERWRITE

## Slide 12: DDLOCK_WRITEONLY
Use D3DVBCAPS_WRITEONLY when creating your VB
Use ONLY this flag
Do NOT USE DDVBCAPS_SYSTEMMEMORY, or you will not get AGP or video memory vertex buffers
  This will require the driver to copy the data into AGP first
  You could have just put it there yourself and saved the work
If you specify this cap, you can only lock w/ DDLOCK_WRITEONLY

## Slide 13: DDLOCK_DISCARDCONTENTS
This flag tells D3D
  “I just need more space, give me a pointer with junk in it, please”
  Specifying this flag allows the driver to “rename” vertex buffers
  You are saying that you don’t want the object back that you just drew, you are saying that you are going to fill up part of this with new data
  This prevents stalling the CPU & GPU

## Slide 14: DDLOCK_NOOVERWRITE
DDLOCK_NOOVERWRITE says “I am just appending data to the VB, no need to stall”
This allows you to append data to a VB without incurring a stall of the GPU & CPU

## Slide 15: Using These Flags Together
Start of Frame – Lock your Dynamic VB with DDLOCK_DISCARDCONTENTS
  Giving you an empty buffer
Fill with data to render
Call Unlock(), then DrawIndexedPrimitiveVB()
Now, as long as there is room in the VB,
  Lock with DDLOCK_NOOVERWRITE
  Append Data into VB pointer
  Unlock(), and DIPVB()
If you run out of room, just lock the SAME VB with the DDLOCK_DISCARDCONTENTS and repeat

## Slide 16: Other Dynamic VB tips
Only use ONE dynamic VB
  An issue with DX7 requires this for performance
  This implies using the largest FVF you need
Send triangles in large batches if you can
NEVER use DrawPrimitive, or DrawIndexedPrimitive, even for Text
  It will ALWAYS cause a stall of the GPU & CPU
Check out your system’s AGP perf with BenMark from our website
  GeForce should get 14 million tps @ AGP2X
  GeForce2 ~22 million w/ AGP 4x

## Slide 17: Other VB Perf Tips
Changing VB is more expensive than changing textures – this is an API thing, not the HW
Never do your own VB “round robin” – that’s what the DDLOCK_DISCARDCONTENTS flag is for
Never use ONLY DDLOCK_DISCARDCONTENTS, there are only so many “rename” buffers – use appending, too
Use only one or two static VBs, and use index lists for different objects within them
Write into DynamicVBs sequentially for AGP write-combining performance

## Slide 18: Source Code
I wrote an extremely lightweight wrapper for correct Dynamic VB functionality
On NVIDIA’s Developer Website
One for C++ heads ( like me )
  DynamicVB.hpp
One for C types
  DynamicVB.h

## Slide 19: Other Optimizations : Culling
The CPU is still needed for gross culling
  View Frustum
    Sphere, AABB, OBB, Cone, Cylinder
  Occlusion
    Don’t use span buffers or C-buffer – too much CPU work
  Light Culling
    Turn off lights that are too far away to affect the object
    Turn point lights into directional if far away
  Fog Culling
    Turn off fog if objects are too far from the fog plane

## Slide 20: Culling and Clipping
Do gross culling on the CPU, but leave the Clipping to the GPU
Expect H/W clipping to be fast ( GeForce clipping is essentially free )
Expect guard band clipping to be very fast
Don’t cull individual polys unless you cull them very early and they are quite expensive
  Culling should be at the model or hierarchy level
  For world geometry at the BSP Leaf or OctTree cube level
H/W will clip out 1.0 < z < 0.0

## Slide 21: Other Optimizations : LOD
Use the CPU to perform gross LOD
  For terrain, don’t use ROAM – too CPU heavy – cheaper to just draw the darn triangles than to figure out which ones to draw and which to skip
  If you do adaptive terrain, do one where you
    A) don’t track previous frame’s terrain
    B) Don’t do screen space error for every triangle
    C) Can ‘quit’ at a high enough level to keep large batch sizes – Quadtree approaches
Don’t do View-dependent progressive meshes
  Again, too much CPU work
View Independent Progressive Meshes look great and are trivial to use with vertex buffers

## Slide 22: Other Optimizations : LOD
Never try to scale to frame rate by adding or removing triangles in small groups on a T&L card
  You are just wasting CPU time
  90% of frame rate drops are CPU or fill-bound, not triangle bound
  Do less LOD calculations when frame rate drops, not more, save the CPU time
  Reduce depth of volumetric effects, especially when player is near
  Reduce particle counts, especially when player is inside the particle system
    Player won’t notice

## Slide 23: Other Optimizations : Lighting
If multi-pass, you often don’t need it on for both passes
Turn on & off lights per object based on distance from light
Turn off per-vertex material properties if you don’t need them
  Using the per-vertex diffuse for the diffuse material is expensive – use it wisely
Turn off local viewer for specular lighting if not needed
  If you are not sure, you probably wouldn’t notice
Turn off SpecularEnable if you aren’t using specular for this pass

## Slide 24: Other Optimizations : Vertex Cache
GeForce GPUS have a ~10 entry FIFO vertex cache
  Post-transformed vertices
If you reuse an indexed triangle within 10 vertices, you save the AGP B/W & transform cost
If you don’t index, or don’t re-use, you pay both AGP & transform again
The fastest primitive is indexed strips, sometimes only the cost of one short per triangle if all reside in cache
Use the NVStripifer on our website to optimize your models

## Slide 25: Other Optimizations : Triangle Size
Little known facts
  Every app is fillbound
  Every app is Xform or setup bound
  - In different parts of the same scene
  Two Engines in parallel – vertex and pixel
Given fill rate, b/w and max xform/setup rate you can determine what the optimal triangle size is for a GPU
  For GeForce, with a few lights on it’s about 100 pixel triangles
  Bigger Tris get you temporarily fill bound
  Smaller Tris get you vertex bound
  More expensive vertices ( more lights or xform work ) need bigger triangles to balance out

## Slide 26: Other Optimizations : Triangle Size
If you are temporarily fill bound ( Tri too big ), you lose xform rate
If you are xform bound ( xformed vertex cache is full ) you loose potential fill rate
This is one reason why you may not see the optimal vertex or fill rate
  If one engine is backed up, the other will eventually idle – and you never get this time back
  When you are drawing the sky, you lose potential triangles
  This means that you can tessellate down to the optimal triangle size in these cases for FREE

## Slide 27: Other Optimizations : Stat Driver
NVIDIA has provided a Statistics Driver for registered developers
  Written by Ken Hurley
You install two parts
  A monitoring program
  A special stats driver
You start the monitoring and then run your app
  Or, you can use a hotkey to toggle the stats collection
Quit your app and see where you are forcing a SpinLock()
  This means the CPU & GPU are idle

## Slide 28: Stats Driver
SpinLock() means the CPU is waiting on the GPU to finish with something
  Usually a shared resource
Most apps spend quite a bit of time here
  This time is totally wasted!
The Stat Driver monitor will tell you where your d3d & driver CPU time is going
Your app should be spending > 60% of the Driver time in DrawIndexedPrimitiveVB
SpinLock() should be < 5%
  The log file can help you track down the culprit

## Slide 29: Summary
T&L is Faster, but it is different
  The first time you port to DX7, you will almost certainly do it wrong! ;(
Use Static VBs for static geometry
Stream vertex data through DynamicVBs
Use the stat driver often when working on rendering code
  Take out stalls as soon as they are introduced
    Texture Locks
    FB or ZB Locks
    VB Locks w/out proper flags
    DrawPrimitive or DIP, not the VB calls

## Slide 30: Questions…
?
Sim Dietrich
Sim.dietrich@nvidia.com